## Slide 1
EG334S · INDIVIDUAL PRESENTATION
Designing Addressing and Routing
CIDR planning, route ownership and public-subnet reachability
across three cloud cells
Adelene
Team Member · Addressing & Routing
TEAM REVIEW · proposed focus · 3 cells · 2 IPSec tunnels
Notes: Open with the outcome and state that ownership is proposed pending team confirmation.
[Sources]
- EG334S Project Information.pdf, project brief and assessment requirements.
- Presentation Assessment Rubrics.pdf, organisation, supporting materials, constraints and Q&A criteria.
- EG334S Project Report TEAM REVIEW.docx, architecture, implementation, test and problem records.
- project.bernardtay.work, dated architecture, inventory, monitoring and recovery evidence.
[/Sources]

## Slide 2
WHAT I WILL COVER
Agenda
1
The address plan
Three non-overlapping /16 networks
2
Subnet design
Workload, public and gateway separation
3
Route ownership
Static routes and propagated routes
4
The public server
How the Ireland workload is reached
5
Constraints & diagnosis
Why tunnel UP does not mean traffic flows
6
Verification
ICMP, TTL and HTTP evidence
My slice
IP addressing
Subnet design
Route tables
Propagation
Public web server
Notes: Explain how this agenda supports IP addressing, routing and the public-subnet web server.
[Sources]
- EG334S Project Information.pdf, project brief and assessment requirements.
- Presentation Assessment Rubrics.pdf, organisation, supporting materials, constraints and Q&A criteria.
- EG334S Project Report TEAM REVIEW.docx, architecture, implementation, test and problem records.
- project.bernardtay.work, dated architecture, inventory, monitoring and recovery evidence.
[/Sources]

## Slide 3
SECTION 1 — CONTEXT
Three cells, two tunnels
Simulated on-prem
AWS us-east-1 · N. Virginia
10.0.0.0/16
strongSwan customer gateway
+ test server
AWS public cloud
AWS eu-west-1 · Ireland
10.1.0.0/16
Apache web server
THE HUB — both tunnels land here
Azure
southeastasia · Singapore
10.2.0.0/16
nginx web server
VPN #1
~69 ms
VPN #2
~189 ms
Both tunnels are IPSec over the public internet. The difference in latency is physical distance, nothing else.
Every ICMP reply came back with ttl=254 — decremented from 255 — which proves the packet crossed a gateway rather than being answered locally. That is how I know the tunnel is genuinely carrying the traffic.
Notes: Use the three-cell diagram for orientation. Point out both VPNs and the non-transitive boundary.
[Sources]
- EG334S Project Information.pdf, project brief and assessment requirements.
- Presentation Assessment Rubrics.pdf, organisation, supporting materials, constraints and Q&A criteria.
- EG334S Project Report TEAM REVIEW.docx, architecture, implementation, test and problem records.
- project.bernardtay.work, dated architecture, inventory, monitoring and recovery evidence.
[/Sources]

## Slide 4
SECTION 2 — ADDRESSING
Non-overlapping CIDRs made routing possible
Address rule
One /16 per cell
Virginia owns 10.0.0.0/16, Ireland owns 10.1.0.0/16 and Azure owns 10.2.0.0/16.
Routing rule
Every remote prefix has one next hop
Static routes express intent at the spokes; route propagation lets the Ireland hub learn both remote networks from its VGW.
Why the sequence matters
Subnets and routes inherit from the CIDR plan. Locking the ranges first prevents the most common VPN symptom: tunnel UP, but no usable path.
10.0.0.0/16
on-prem
10.1.0.0/16
AWS public
10.2.0.0/16
Azure
Notes: Connect the design sequence to IP addressing, routing and the public-subnet web server.
[Sources]
- EG334S Project Information.pdf, project brief and assessment requirements.
- Presentation Assessment Rubrics.pdf, organisation, supporting materials, constraints and Q&A criteria.
- EG334S Project Report TEAM REVIEW.docx, architecture, implementation, test and problem records.
- project.bernardtay.work, dated architecture, inventory, monitoring and recovery evidence.
[/Sources]

## Slide 5
SECTION 2 — DELIVERY
Where we ended up
1
CIDR scheme locked
Three non-overlapping ranges
DONE
2
All three networks live
2 AWS VPCs + Azure VNet
DONE
3
First tunnel passing traffic
on-prem ↔ AWS, 0% loss
DONE
4
Multi-cloud proven
ICMP + HTTP across providers
DONE
5
Assessed demonstration
this session
NEXT
6
Fully decommissioned
by 30 Aug 23:59
NEXT
Four of six milestones achieved — and we hit them roughly two weeks ahead of the planned dates.
The time we bought went into testing properly and capturing evidence while the system was live — not into extra features.
Notes: Use milestones as shared project evidence; do not imply sole ownership of team work.
[Sources]
- EG334S Project Information.pdf, project brief and assessment requirements.
- Presentation Assessment Rubrics.pdf, organisation, supporting materials, constraints and Q&A criteria.
- EG334S Project Report TEAM REVIEW.docx, architecture, implementation, test and problem records.
- project.bernardtay.work, dated architecture, inventory, monitoring and recovery evidence.
[/Sources]

## Slide 6
SECTION 3 — MY SLICE
Three address spaces, one unambiguous plan
1
Virginia: 10.0.0.0/16
The simulated on-premises cell includes a public gateway subnet and a private test-server subnet.
2
Ireland: 10.1.0.0/16
The public workload subnet hosts the Apache server; a separate 10.1.2.0/24 subnet is reserved for recovery.
3
Azure: 10.2.0.0/16
The workload subnet is distinct from GatewaySubnet 10.2.255.0/27, which is reserved for the managed VPN gateway.
No range overlaps another, so the same addressing table drives routes, security rules and test expectations.
Notes: Defend the member-specific focus: IP addressing, routing and the public-subnet web server.
[Sources]
- EG334S Project Information.pdf, project brief and assessment requirements.
- Presentation Assessment Rubrics.pdf, organisation, supporting materials, constraints and Q&A criteria.
- EG334S Project Report TEAM REVIEW.docx, architecture, implementation, test and problem records.
- project.bernardtay.work, dated architecture, inventory, monitoring and recovery evidence.
[/Sources]

## Slide 7
SECTION 4 — MY SLICE
Routes split between static intent and managed propagation
Each route answers one question: for this destination prefix, which gateway or interface owns the next hop?
Virginia
10.1.0.0/16
route points to strongSwan EC2
Ireland
propagated
VGW learns both spoke prefixes
Azure
10.1.0.0/16
declared through the local network gateway
254
observed TTL
proves a gateway hop occurred
0%
packet loss
on the demonstrated paths
HTTP
application test
Azure VM to Ireland Apache
The insight: route tables prove intent; traffic tests prove outcome.
I read both together because a correctly configured tunnel can still have a missing or misdirected route.
Notes: Explain the operational measure and the trade-off behind it.
[Sources]
- EG334S Project Information.pdf, project brief and assessment requirements.
- Presentation Assessment Rubrics.pdf, organisation, supporting materials, constraints and Q&A criteria.
- EG334S Project Report TEAM REVIEW.docx, architecture, implementation, test and problem records.
- project.bernardtay.work, dated architecture, inventory, monitoring and recovery evidence.
[/Sources]

## Slide 8
SECTION 5 — CONSTRAINTS AND DIAGNOSIS
Addressing and routing failure modes
Tunnel UP, traffic DOWN
The control plane can be healthy while a route, security rule or source prefix is wrong.
WORKAROUND
Check accepted routes, both directions of the path, security scope and the actual source address.
GatewaySubnet has special rules
It exists for Azure’s managed VPN gateway, not ordinary workloads.
WORKAROUND
Kept it dedicated at 10.2.255.0/27 and applied the NSG only to the workload subnet.
A public IP is not the recovery identity
Replacing an EC2 service can change its instance and public endpoint.
WORKAROUND
Use a stable private DNS name inside the VPC so recovery does not require peer route changes.
The troubleshooting order is deliberate: address, route, security, tunnel telemetry, then application.
Notes: State each platform constraint, workaround and residual risk explicitly.
[Sources]
- EG334S Project Information.pdf, project brief and assessment requirements.
- Presentation Assessment Rubrics.pdf, organisation, supporting materials, constraints and Q&A criteria.
- EG334S Project Report TEAM REVIEW.docx, architecture, implementation, test and problem records.
- project.bernardtay.work, dated architecture, inventory, monitoring and recovery evidence.
[/Sources]

## Slide 9
SECTION 6 — THE ROUTING FINDING
A valid route to the hub
is not a route through the hub.
Expected: Virginia cannot transit Ireland to Azure
The destination prefix has no supported transitive next hop.
VGW route propagation teaches the Ireland VPC how to reach both spokes. It does not convert VGW into a router between the two VPN connections.
Why this matters
The route table and negative test together define the real connectivity boundary.
If transit is required
Introduce Transit Gateway or a routed appliance, update route ownership and repeat every positive and negative test.
Notes: Separate expected architectural behaviour from an implementation fault.
[Sources]
- EG334S Project Information.pdf, project brief and assessment requirements.
- Presentation Assessment Rubrics.pdf, organisation, supporting materials, constraints and Q&A criteria.
- EG334S Project Report TEAM REVIEW.docx, architecture, implementation, test and problem records.
- project.bernardtay.work, dated architecture, inventory, monitoring and recovery evidence.
[/Sources]

## Slide 10
SECTION 6 — RESULTS
How I know it works
I tested at two levels for each tunnel, because a tunnel can report UP while carrying no traffic at all.
0%
packet loss, both tunnels
254
ttl — proves it was routed
6/6
tests with expected result
2
providers, one HTTP request
The strongest single result
curl http://10.1.1.90 → <h1>EG334S AWS Public Cloud Web Server (eu-west-1)</h1>
A complete application request, issued from a virtual machine in Azure in Singapore, crossed an encrypted tunnel over the public internet, was served by Apache in AWS in Ireland, and returned by the same path.
Control plane
Provider telemetry: both tunnels report UP with an accepted route
Data plane
ICMP verified in both directions, 0% loss, ttl 254
Application layer
HTTP served across two cloud providers
Negative test
Transitive path fails, as designed and documented
Notes: Walk through control-plane, data-plane and application-layer evidence.
[Sources]
- EG334S Project Information.pdf, project brief and assessment requirements.
- Presentation Assessment Rubrics.pdf, organisation, supporting materials, constraints and Q&A criteria.
- EG334S Project Report TEAM REVIEW.docx, architecture, implementation, test and problem records.
- project.bernardtay.work, dated architecture, inventory, monitoring and recovery evidence.
[/Sources]

## Slide 11
SECTION 6 — RECOVERY ROUTING
Private DNS keeps recovery routing stable
1
Stable name
The recovery pattern uses a private DNS record for the hub application rather than treating an EC2 public IP as permanent.
2
Measured result
The application returned in 4m 04s, inside the accepted 10-minute objective.
3
Route impact
The standby remains inside the Ireland VPC, so existing VPN and VGW routes do not need to change.
4
Limit of the test
This validates application reachability after EC2 recovery. It does not validate a failed VGW, VPN connection or AWS region.
Notes: Use the precise term automated recoverability, not full High Availability.
[Sources]
- EG334S Project Information.pdf, project brief and assessment requirements.
- Presentation Assessment Rubrics.pdf, organisation, supporting materials, constraints and Q&A criteria.
- EG334S Project Report TEAM REVIEW.docx, architecture, implementation, test and problem records.
- project.bernardtay.work, dated architecture, inventory, monitoring and recovery evidence.
[/Sources]

## Slide 12
PREPARED ANSWERS
Questions I expect
Q
Why use /16 networks?
They are easy to distinguish, do not overlap and leave room for workload, gateway and recovery subnets without redesign.
Q
Which routes are static and which are propagated?
The spokes declare remote prefixes; the Ireland VPC uses VGW route propagation to learn both spoke networks.
Q
Why does ttl=254 matter?
The response began at 255 and lost one hop, showing that a gateway routed the packet rather than a local host answering.
Q
Can the spokes reach each other?
No. VGW does not provide transitive routing between the two VPN connections.
Q
Why keep GatewaySubnet separate?
Azure reserves it for the managed VPN gateway. Workload controls belong on the workload subnet.
Q
How does recovery avoid route changes?
The replacement service stays in the Ireland VPC and uses a stable private DNS identity.
Notes: Answer directly, then cite the diagram, report section or dated evidence.
[Sources]
- EG334S Project Information.pdf, project brief and assessment requirements.
- Presentation Assessment Rubrics.pdf, organisation, supporting materials, constraints and Q&A criteria.
- EG334S Project Report TEAM REVIEW.docx, architecture, implementation, test and problem records.
- project.bernardtay.work, dated architecture, inventory, monitoring and recovery evidence.
[/Sources]

## Slide 13
IN SUMMARY
The routing story starts
with the address plan.
1
Three non-overlapping /16 networks make every route, rule and test expectation unambiguous.
2
Static spoke routes and Ireland VGW propagation establish the two intended hub paths.
3
ICMP, TTL and HTTP evidence prove outcome; the negative transit test defines the boundary.
Thank you — I can trace any tested packet from source CIDR to next hop and destination.
Notes: Close with three claims: what works, what boundary remains, and what is still provisional.
[Sources]
- EG334S Project Information.pdf, project brief and assessment requirements.
- Presentation Assessment Rubrics.pdf, organisation, supporting materials, constraints and Q&A criteria.
- EG334S Project Report TEAM REVIEW.docx, architecture, implementation, test and problem records.
- project.bernardtay.work, dated architecture, inventory, monitoring and recovery evidence.
[/Sources]