## Slide 1
EG334S · INDIVIDUAL PRESENTATION
Building the Multi-Cloud Network
VPC/VNet construction, gateway roles and two IPSec paths
across AWS and Azure
Jeff
Team Member · Network Build & VPN
TEAM REVIEW · proposed focus · 3 cells · 2 IPSec tunnels
Notes: Open with the outcome and state that ownership is proposed pending team confirmation.
[Sources]
- EG334S Project Information.pdf, project brief and assessment requirements.
- Presentation Assessment Rubrics.pdf, organisation, supporting materials, constraints and Q&A criteria.
- EG334S Project Report TEAM REVIEW.docx, architecture, implementation, test and problem records.
- project.bernardtay.work, dated architecture, inventory, monitoring and recovery evidence.
[/Sources]

## Slide 2
WHAT I WILL COVER
Agenda
1
The topology
Three cells and two encrypted paths
2
Network foundations
VPCs, VNet, subnets and gateways
3
VPN #1
strongSwan customer gateway to AWS VGW
4
VPN #2
Azure VPN gateway to the same AWS VGW
5
Routing & constraints
Static intent, propagation and no transit
6
Verification
Control plane, data plane and HTTP evidence
My slice
VPC/VNet build
VPN #1 and VPN #2
VGW Ireland
Customer gateway
Routing evidence
Notes: Explain how this agenda supports VPC/VNet build, both VPNs, Ireland VGW and Virginia customer gateway.
[Sources]
- EG334S Project Information.pdf, project brief and assessment requirements.
- Presentation Assessment Rubrics.pdf, organisation, supporting materials, constraints and Q&A criteria.
- EG334S Project Report TEAM REVIEW.docx, architecture, implementation, test and problem records.
- project.bernardtay.work, dated architecture, inventory, monitoring and recovery evidence.
[/Sources]

## Slide 3
SECTION 1 — CONTEXT
Three cells, two tunnels
Simulated on-prem
AWS us-east-1 · N. Virginia
10.0.0.0/16
strongSwan customer gateway
+ test server
AWS public cloud
AWS eu-west-1 · Ireland
10.1.0.0/16
Apache web server
THE HUB — both tunnels land here
Azure
southeastasia · Singapore
10.2.0.0/16
nginx web server
VPN #1
~69 ms
VPN #2
~189 ms
Both tunnels are IPSec over the public internet. The difference in latency is physical distance, nothing else.
Every ICMP reply came back with ttl=254 — decremented from 255 — which proves the packet crossed a gateway rather than being answered locally. That is how I know the tunnel is genuinely carrying the traffic.
Notes: Use the three-cell diagram for orientation. Point out both VPNs and the non-transitive boundary.
[Sources]
- EG334S Project Information.pdf, project brief and assessment requirements.
- Presentation Assessment Rubrics.pdf, organisation, supporting materials, constraints and Q&A criteria.
- EG334S Project Report TEAM REVIEW.docx, architecture, implementation, test and problem records.
- project.bernardtay.work, dated architecture, inventory, monitoring and recovery evidence.
[/Sources]

## Slide 4
SECTION 2 — NETWORK BUILD
Each VPN needs two different gateway roles
AWS side
VGW in Ireland
The Virtual Private Gateway attaches to the hub VPC and terminates both site-to-site VPN connections.
Peer side
CGW in Virginia + LNG/VNG in Azure
Virginia supplies strongSwan as the customer gateway; Azure uses a Local Network Gateway and managed VPN Gateway.
Build order prevents false troubleshooting
Create non-overlapping networks and subnets first, then compute, stable public endpoints, gateways, VPN connections, routes and finally data-plane tests.
10.0.0.0/16
on-prem
10.1.0.0/16
AWS public
10.2.0.0/16
Azure
Notes: Connect the design sequence to VPC/VNet build, both VPNs, Ireland VGW and Virginia customer gateway.
[Sources]
- EG334S Project Information.pdf, project brief and assessment requirements.
- Presentation Assessment Rubrics.pdf, organisation, supporting materials, constraints and Q&A criteria.
- EG334S Project Report TEAM REVIEW.docx, architecture, implementation, test and problem records.
- project.bernardtay.work, dated architecture, inventory, monitoring and recovery evidence.
[/Sources]

## Slide 5
SECTION 2 — DELIVERY
Where we ended up
1
CIDR scheme locked
Three non-overlapping ranges
DONE
2
All three networks live
2 AWS VPCs + Azure VNet
DONE
3
First tunnel passing traffic
on-prem ↔ AWS, 0% loss
DONE
4
Multi-cloud proven
ICMP + HTTP across providers
DONE
5
Assessed demonstration
this session
NEXT
6
Fully decommissioned
by 30 Aug 23:59
NEXT
Four of six milestones achieved — and we hit them roughly two weeks ahead of the planned dates.
The time we bought went into testing properly and capturing evidence while the system was live — not into extra features.
Notes: Use milestones as shared project evidence; do not imply sole ownership of team work.
[Sources]
- EG334S Project Information.pdf, project brief and assessment requirements.
- Presentation Assessment Rubrics.pdf, organisation, supporting materials, constraints and Q&A criteria.
- EG334S Project Report TEAM REVIEW.docx, architecture, implementation, test and problem records.
- project.bernardtay.work, dated architecture, inventory, monitoring and recovery evidence.
[/Sources]

## Slide 6
SECTION 3 — MY SLICE
VPN #1: Virginia strongSwan to Ireland VGW
1
Customer gateway role
The EC2 instance represents the on-premises VPN appliance. Its Elastic IP is registered with AWS as the customer gateway endpoint.
2
Packet forwarding
SourceDestCheck is disabled and IP forwarding is enabled so the instance can route packets not addressed to itself.
3
Tunnel parameters
The downloaded AWS configuration supplies peer addresses and crypto settings; the pre-shared key is kept outside the repository.
The workload route for 10.1.0.0/16 points to the strongSwan gateway, not directly to an internet gateway.
Notes: Defend the member-specific focus: VPC/VNet build, both VPNs, Ireland VGW and Virginia customer gateway.
[Sources]
- EG334S Project Information.pdf, project brief and assessment requirements.
- Presentation Assessment Rubrics.pdf, organisation, supporting materials, constraints and Q&A criteria.
- EG334S Project Report TEAM REVIEW.docx, architecture, implementation, test and problem records.
- project.bernardtay.work, dated architecture, inventory, monitoring and recovery evidence.
[/Sources]

## Slide 7
SECTION 4 — MY SLICE
VPN #2: Azure and AWS meet on route-based IPSec
Azure provisioning takes longer, so the VNet, GatewaySubnet and public IP must exist before the VPN Gateway is created.
AWS object
VPN connection
Terminates on the existing Ireland VGW.
Azure objects
LNG + VNG
Define the AWS peer and managed endpoint.
IKEv2
mode
route-based IPSec
/27
GatewaySubnet
dedicated to the managed gateway
static
routing
remote prefixes declared
189 ms
observed RTT
Singapore ↔ Ireland
The insight: an UP tunnel is only a control-plane signal.
I verified routing with ICMP in both directions and HTTP from Azure to the Ireland web server.
Notes: Explain the operational measure and the trade-off behind it.
[Sources]
- EG334S Project Information.pdf, project brief and assessment requirements.
- Presentation Assessment Rubrics.pdf, organisation, supporting materials, constraints and Q&A criteria.
- EG334S Project Report TEAM REVIEW.docx, architecture, implementation, test and problem records.
- project.bernardtay.work, dated architecture, inventory, monitoring and recovery evidence.
[/Sources]

## Slide 8
SECTION 5 — CONSTRAINTS AND WORKAROUNDS
VPN build constraints, and how I resolved them
AWS supplies only one end
A VGW cannot create the Virginia peer that the design needs.
WORKAROUND
Built the peer on EC2 with strongSwan, a stable Elastic IP and forwarding enabled.
Azure gateway provisioning is slow
Repeated delete/recreate cycles waste time and cost money.
WORKAROUND
Separated network, gateway and VPN steps so a configuration change does not rebuild the whole VNet.
Secrets must not enter source control
Provider downloads contain a pre-shared key required by the tunnel.
WORKAROUND
Stored the key only in the runtime configuration and published a redacted example for the team.
The practical lesson: isolate long-lived gateways and secrets from frequently changed workload code.
Notes: State each platform constraint, workaround and residual risk explicitly.
[Sources]
- EG334S Project Information.pdf, project brief and assessment requirements.
- Presentation Assessment Rubrics.pdf, organisation, supporting materials, constraints and Q&A criteria.
- EG334S Project Report TEAM REVIEW.docx, architecture, implementation, test and problem records.
- project.bernardtay.work, dated architecture, inventory, monitoring and recovery evidence.
[/Sources]

## Slide 9
SECTION 6 — THE NETWORK FINDING
Two VPNs can be healthy.
Transit can still be unavailable.
VPN #1 UP + VPN #2 UP ≠ spoke-to-spoke path
This is expected VGW behaviour.
The Ireland VGW learns routes for both connections but does not re-forward traffic arriving from one VPN out through the other.
How I prove a tunnel
Check provider state, accepted routes, bidirectional ICMP and an application request. No single signal is sufficient.
If transit is required
Replace VGW with Transit Gateway or a routed appliance design, then account for new routing, security and cost.
Notes: Separate expected architectural behaviour from an implementation fault.
[Sources]
- EG334S Project Information.pdf, project brief and assessment requirements.
- Presentation Assessment Rubrics.pdf, organisation, supporting materials, constraints and Q&A criteria.
- EG334S Project Report TEAM REVIEW.docx, architecture, implementation, test and problem records.
- project.bernardtay.work, dated architecture, inventory, monitoring and recovery evidence.
[/Sources]

## Slide 10
SECTION 6 — RESULTS
How I know it works
I tested at two levels for each tunnel, because a tunnel can report UP while carrying no traffic at all.
0%
packet loss, both tunnels
254
ttl — proves it was routed
6/6
tests with expected result
2
providers, one HTTP request
The strongest single result
curl http://10.1.1.90 → <h1>EG334S AWS Public Cloud Web Server (eu-west-1)</h1>
A complete application request, issued from a virtual machine in Azure in Singapore, crossed an encrypted tunnel over the public internet, was served by Apache in AWS in Ireland, and returned by the same path.
Control plane
Provider telemetry: both tunnels report UP with an accepted route
Data plane
ICMP verified in both directions, 0% loss, ttl 254
Application layer
HTTP served across two cloud providers
Negative test
Transitive path fails, as designed and documented
Notes: Walk through control-plane, data-plane and application-layer evidence.
[Sources]
- EG334S Project Information.pdf, project brief and assessment requirements.
- Presentation Assessment Rubrics.pdf, organisation, supporting materials, constraints and Q&A criteria.
- EG334S Project Report TEAM REVIEW.docx, architecture, implementation, test and problem records.
- project.bernardtay.work, dated architecture, inventory, monitoring and recovery evidence.
[/Sources]

## Slide 11
SECTION 6 — RECOVERY BOUNDARY
The standby must never own the VGW or VPNs
1
Separation rule
The primary and recovery stacks are separate. Shared VPC, VGW and VPN connections remain outside the recovery stack.
2
Measured result
The Ireland EC2 service recovered in 4m 04s without rebuilding either VPN connection.
3
Network implication
Stable private DNS and existing routes allow the recovered service to take over without changing peer VPN configuration.
4
Limit of the test
A VGW, VPN or regional failure was not simulated. This is application recovery, not network High Availability.
Notes: Use the precise term automated recoverability, not full High Availability.
[Sources]
- EG334S Project Information.pdf, project brief and assessment requirements.
- Presentation Assessment Rubrics.pdf, organisation, supporting materials, constraints and Q&A criteria.
- EG334S Project Report TEAM REVIEW.docx, architecture, implementation, test and problem records.
- project.bernardtay.work, dated architecture, inventory, monitoring and recovery evidence.
[/Sources]

## Slide 12
PREPARED ANSWERS
Questions I expect
Q
What is the difference between VGW and CGW?
VGW is the AWS-managed termination attached to the hub VPC. CGW represents the remote VPN device, here the strongSwan EC2 endpoint.
Q
Why disable SourceDestCheck?
A normal EC2 instance only handles traffic addressed to itself. A router must forward packets for other hosts.
Q
How do you know the VPN carries traffic?
I combine tunnel state and learned routes with bidirectional ping and an HTTP request across the encrypted path.
Q
Why use IKEv1 for one path and IKEv2 for the other?
The strongSwan path follows the downloaded AWS configuration; Azure’s route-based gateway uses the supported IKEv2 profile.
Q
Why is there no Virginia-to-Azure path?
AWS VGW is non-transitive. Both peers reach the Ireland hub, but not each other.
Q
Where is the pre-shared key?
Only in the protected runtime configuration. It is not stored in the dashboard, deck or repository.
Notes: Answer directly, then cite the diagram, report section or dated evidence.
[Sources]
- EG334S Project Information.pdf, project brief and assessment requirements.
- Presentation Assessment Rubrics.pdf, organisation, supporting materials, constraints and Q&A criteria.
- EG334S Project Report TEAM REVIEW.docx, architecture, implementation, test and problem records.
- project.bernardtay.work, dated architecture, inventory, monitoring and recovery evidence.
[/Sources]

## Slide 13
IN SUMMARY
Both VPNs are explainable
from endpoint to evidence.
1
Virginia uses strongSwan as the customer gateway; Azure uses a managed route-based VPN gateway.
2
The Ireland VGW terminates both connections while routing remains intentionally non-transitive.
3
Control-plane state, bidirectional ICMP and HTTP together provide defensible proof.
Thank you — I can walk through either VPN build and its troubleshooting sequence.
Notes: Close with three claims: what works, what boundary remains, and what is still provisional.
[Sources]
- EG334S Project Information.pdf, project brief and assessment requirements.
- Presentation Assessment Rubrics.pdf, organisation, supporting materials, constraints and Q&A criteria.
- EG334S Project Report TEAM REVIEW.docx, architecture, implementation, test and problem records.
- project.bernardtay.work, dated architecture, inventory, monitoring and recovery evidence.
[/Sources]