## Slide 1
EG334S · INDIVIDUAL PRESENTATION
Operating the Virginia Private Cell
Private server, DNS/DHCP behaviour and strongSwan routing
inside the simulated enterprise edge
Soo Fern
Team Member · Virginia Cell Operations
TEAM REVIEW · proposed focus · 3 cells · 2 IPSec tunnels
Notes: Open with the outcome and state that ownership is proposed pending team confirmation.
[Sources]
- EG334S Project Information.pdf, project brief and assessment requirements.
- Presentation Assessment Rubrics.pdf, organisation, supporting materials, constraints and Q&A criteria.
- EG334S Project Report TEAM REVIEW.docx, architecture, implementation, test and problem records.
- project.bernardtay.work, dated architecture, inventory, monitoring and recovery evidence.
[/Sources]

## Slide 2
WHAT I WILL COVER
Agenda
1
The Virginia role
How AWS simulates the on-premises edge
2
Compute design
Gateway host and private test server
3
DNS & DHCP
How instances receive identity and resolution
4
strongSwan routing
Forwarding traffic into VPN #1
5
Problems & solutions
A repeatable troubleshooting sequence
6
Verification
What proves the private cell works
My slice
Virginia cell
Private server
DNS and DHCP
strongSwan routing
Troubleshooting
Notes: Explain how this agenda supports Virginia private server, DNS/DHCP and problems-and-solutions log.
[Sources]
- EG334S Project Information.pdf, project brief and assessment requirements.
- Presentation Assessment Rubrics.pdf, organisation, supporting materials, constraints and Q&A criteria.
- EG334S Project Report TEAM REVIEW.docx, architecture, implementation, test and problem records.
- project.bernardtay.work, dated architecture, inventory, monitoring and recovery evidence.
[/Sources]

## Slide 3
SECTION 1 — CONTEXT
Three cells, two tunnels
Simulated on-prem
AWS us-east-1 · N. Virginia
10.0.0.0/16
strongSwan customer gateway
+ test server
AWS public cloud
AWS eu-west-1 · Ireland
10.1.0.0/16
Apache web server
THE HUB — both tunnels land here
Azure
southeastasia · Singapore
10.2.0.0/16
nginx web server
VPN #1
~69 ms
VPN #2
~189 ms
Both tunnels are IPSec over the public internet. The difference in latency is physical distance, nothing else.
Every ICMP reply came back with ttl=254 — decremented from 255 — which proves the packet crossed a gateway rather than being answered locally. That is how I know the tunnel is genuinely carrying the traffic.
Notes: Use the three-cell diagram for orientation. Point out both VPNs and the non-transitive boundary.
[Sources]
- EG334S Project Information.pdf, project brief and assessment requirements.
- Presentation Assessment Rubrics.pdf, organisation, supporting materials, constraints and Q&A criteria.
- EG334S Project Report TEAM REVIEW.docx, architecture, implementation, test and problem records.
- project.bernardtay.work, dated architecture, inventory, monitoring and recovery evidence.
[/Sources]

## Slide 4
SECTION 2 — VIRGINIA CELL
Two EC2 roles keep routing separate from testing
Gateway host
strongSwan router
The public EC2 instance owns the stable Elastic IP, terminates IPSec and forwards traffic between the private cell and Ireland.
Workload host
private test server
The test server uses private addressing and the VPC resolver. It generates clean evidence without also being the VPN endpoint.
Why role separation matters
A gateway fault and an application fault produce different symptoms. Separate hosts make packet paths, security rules and recovery steps easier to explain.
10.0.0.0/16
on-prem
10.1.0.0/16
AWS public
10.2.0.0/16
Azure
Notes: Connect the design sequence to Virginia private server, DNS/DHCP and problems-and-solutions log.
[Sources]
- EG334S Project Information.pdf, project brief and assessment requirements.
- Presentation Assessment Rubrics.pdf, organisation, supporting materials, constraints and Q&A criteria.
- EG334S Project Report TEAM REVIEW.docx, architecture, implementation, test and problem records.
- project.bernardtay.work, dated architecture, inventory, monitoring and recovery evidence.
[/Sources]

## Slide 5
SECTION 2 — DELIVERY
Where we ended up
1
CIDR scheme locked
Three non-overlapping ranges
DONE
2
All three networks live
2 AWS VPCs + Azure VNet
DONE
3
First tunnel passing traffic
on-prem ↔ AWS, 0% loss
DONE
4
Multi-cloud proven
ICMP + HTTP across providers
DONE
5
Assessed demonstration
this session
NEXT
6
Fully decommissioned
by 30 Aug 23:59
NEXT
Four of six milestones achieved — and we hit them roughly two weeks ahead of the planned dates.
The time we bought went into testing properly and capturing evidence while the system was live — not into extra features.
Notes: Use milestones as shared project evidence; do not imply sole ownership of team work.
[Sources]
- EG334S Project Information.pdf, project brief and assessment requirements.
- Presentation Assessment Rubrics.pdf, organisation, supporting materials, constraints and Q&A criteria.
- EG334S Project Report TEAM REVIEW.docx, architecture, implementation, test and problem records.
- project.bernardtay.work, dated architecture, inventory, monitoring and recovery evidence.
[/Sources]

## Slide 6
SECTION 3 — MY SLICE
The private test server stays simple by design
1
Private identity
The instance receives its private address and network settings from the VPC subnet through AWS-provided DHCP behaviour.
2
DNS resolution
The VPC resolver supplies internal name resolution. Stable names are safer than memorising replaceable instance addresses.
3
Scoped access
The workload does not need to terminate IPSec. Its security rules allow only the test traffic required by the project.
The server’s job is to originate and receive evidence traffic, not to hide routing complexity inside the application.
Notes: Defend the member-specific focus: Virginia private server, DNS/DHCP and problems-and-solutions log.
[Sources]
- EG334S Project Information.pdf, project brief and assessment requirements.
- Presentation Assessment Rubrics.pdf, organisation, supporting materials, constraints and Q&A criteria.
- EG334S Project Report TEAM REVIEW.docx, architecture, implementation, test and problem records.
- project.bernardtay.work, dated architecture, inventory, monitoring and recovery evidence.
[/Sources]

## Slide 7
SECTION 4 — MY SLICE
strongSwan is the router, not the workload
The gateway joins AWS’s downloaded VPN parameters to ordinary Linux forwarding and VPC routing.
EIP
stable endpoint
registered as the AWS customer gateway
off
SourceDestCheck
allows forwarding for other hosts
on
IP forwarding
moves packets between interfaces
IKE
UDP 500
tunnel negotiation
NAT-T
UDP 4500
IPSec across NAT
route
10.1.0.0/16
next hop is strongSwan
The insight: the VPC route table sends packets to the gateway; strongSwan decides whether they enter the encrypted tunnel.
Both layers must agree. Fixing only the tunnel or only the VPC route leaves the path incomplete.
Notes: Explain the operational measure and the trade-off behind it.
[Sources]
- EG334S Project Information.pdf, project brief and assessment requirements.
- Presentation Assessment Rubrics.pdf, organisation, supporting materials, constraints and Q&A criteria.
- EG334S Project Report TEAM REVIEW.docx, architecture, implementation, test and problem records.
- project.bernardtay.work, dated architecture, inventory, monitoring and recovery evidence.
[/Sources]

## Slide 8
SECTION 5 — PROBLEMS AND SOLUTIONS
Virginia troubleshooting in the right order
Tunnel UP, ping fails
The route may point at the wrong next hop, forwarding may be off, or security scope may exclude the real source.
WORKAROUND
Check VPC route, SourceDestCheck, Linux forwarding, XFRM policy and both security groups.
DNS name fails, IP works
That separates a name-resolution problem from a VPN or routing problem.
WORKAROUND
Query the VPC resolver and compare the returned private address with the intended server.
SSH exposure is too broad
0.0.0.0/0 is convenient for a lab but not a defensible production control.
WORKAROUND
Restrict administration to an approved /32 or use Systems Manager Session Manager.
The problems-and-solutions log records symptom, evidence, root cause, corrective action and retest result.
Notes: State each platform constraint, workaround and residual risk explicitly.
[Sources]
- EG334S Project Information.pdf, project brief and assessment requirements.
- Presentation Assessment Rubrics.pdf, organisation, supporting materials, constraints and Q&A criteria.
- EG334S Project Report TEAM REVIEW.docx, architecture, implementation, test and problem records.
- project.bernardtay.work, dated architecture, inventory, monitoring and recovery evidence.
[/Sources]

## Slide 9
SECTION 6 — THE OPERATIONS FINDING
Control-plane status is not
data-plane proof.
A green VPN icon can coexist with a broken packet path
Troubleshooting must follow the packet.
A successful IKE negotiation proves the peers established security associations. It does not prove the private server has a route, that forwarding works or that return traffic is allowed.
My diagnostic order
DNS → address → VPC route → Linux forwarding → IPSec policy → security scope → return path.
Why this helps the team
Each check removes one failure domain and produces evidence that another member can reproduce.
Notes: Separate expected architectural behaviour from an implementation fault.
[Sources]
- EG334S Project Information.pdf, project brief and assessment requirements.
- Presentation Assessment Rubrics.pdf, organisation, supporting materials, constraints and Q&A criteria.
- EG334S Project Report TEAM REVIEW.docx, architecture, implementation, test and problem records.
- project.bernardtay.work, dated architecture, inventory, monitoring and recovery evidence.
[/Sources]

## Slide 10
SECTION 6 — RESULTS
How I know it works
I tested at two levels for each tunnel, because a tunnel can report UP while carrying no traffic at all.
0%
packet loss, both tunnels
254
ttl — proves it was routed
6/6
tests with expected result
2
providers, one HTTP request
The strongest single result
curl http://10.1.1.90 → <h1>EG334S AWS Public Cloud Web Server (eu-west-1)</h1>
A complete application request, issued from a virtual machine in Azure in Singapore, crossed an encrypted tunnel over the public internet, was served by Apache in AWS in Ireland, and returned by the same path.
Control plane
Provider telemetry: both tunnels report UP with an accepted route
Data plane
ICMP verified in both directions, 0% loss, ttl 254
Application layer
HTTP served across two cloud providers
Negative test
Transitive path fails, as designed and documented
Notes: Walk through control-plane, data-plane and application-layer evidence.
[Sources]
- EG334S Project Information.pdf, project brief and assessment requirements.
- Presentation Assessment Rubrics.pdf, organisation, supporting materials, constraints and Q&A criteria.
- EG334S Project Report TEAM REVIEW.docx, architecture, implementation, test and problem records.
- project.bernardtay.work, dated architecture, inventory, monitoring and recovery evidence.
[/Sources]

## Slide 11
SECTION 6 — RECOVERY VALIDATION
Virginia independently validates hub recovery
1
Scope the check
After the Ireland service is replaced, Virginia can test the same private service identity across VPN #1.
2
Measured result
The hub application recovered in 4m 04s against the accepted 10-minute objective.
3
What remains stable
Virginia’s route and strongSwan tunnel remain unchanged because recovery occurs inside the Ireland VPC.
4
Limit of the claim
The drill did not fail strongSwan, the VGW, VPN #1 or the Virginia region. It is not full High Availability.
Notes: Use the precise term automated recoverability, not full High Availability.
[Sources]
- EG334S Project Information.pdf, project brief and assessment requirements.
- Presentation Assessment Rubrics.pdf, organisation, supporting materials, constraints and Q&A criteria.
- EG334S Project Report TEAM REVIEW.docx, architecture, implementation, test and problem records.
- project.bernardtay.work, dated architecture, inventory, monitoring and recovery evidence.
[/Sources]

## Slide 12
PREPARED ANSWERS
Questions I expect
Q
Why use two EC2 instances in Virginia?
One is the VPN router and one is the private workload. Separation makes routing, testing and troubleshooting clearer.
Q
What does SourceDestCheck do?
It normally prevents EC2 from forwarding traffic for other hosts. A gateway requires it disabled.
Q
Where do DNS and DHCP come from?
AWS VPC services supply subnet configuration and the VPC resolver supplies internal name resolution.
Q
What do you check when the tunnel is UP but ping fails?
Route, forwarding, IPSec policy, security scope and return path—in that order.
Q
Can the private server reach Azure?
No. The Ireland VGW is non-transitive, so VPN #1 does not forward into VPN #2.
Q
How would you tighten administration?
Restrict SSH to an approved /32 or remove inbound SSH and use Systems Manager Session Manager.
Notes: Answer directly, then cite the diagram, report section or dated evidence.
[Sources]
- EG334S Project Information.pdf, project brief and assessment requirements.
- Presentation Assessment Rubrics.pdf, organisation, supporting materials, constraints and Q&A criteria.
- EG334S Project Report TEAM REVIEW.docx, architecture, implementation, test and problem records.
- project.bernardtay.work, dated architecture, inventory, monitoring and recovery evidence.
[/Sources]

## Slide 13
IN SUMMARY
Virginia is a controlled
enterprise-edge simulation.
1
The strongSwan gateway and private test server have separate, explainable responsibilities.
2
VPC routing, Linux forwarding and IPSec policy must all agree before traffic can cross VPN #1.
3
DNS/IP comparison and a fixed troubleshooting order turn symptoms into reproducible evidence.
Thank you — I can demonstrate the Virginia packet path and diagnose each failure domain.
Notes: Close with three claims: what works, what boundary remains, and what is still provisional.
[Sources]
- EG334S Project Information.pdf, project brief and assessment requirements.
- Presentation Assessment Rubrics.pdf, organisation, supporting materials, constraints and Q&A criteria.
- EG334S Project Report TEAM REVIEW.docx, architecture, implementation, test and problem records.
- project.bernardtay.work, dated architecture, inventory, monitoring and recovery evidence.
[/Sources]